## Slide 1: Analog Communication Systems
BECE 304L
Module-1
Lecture: 3 & 4

## Slide 2: Course- modules

## Slide 3: The Electromagnetic Spectrum
The range of electromagnetic signals encompassing all frequencies is referred to as the electromagnetic spectrum.

## Slide 4: The Electromagnetic Spectrum
Figure 1-13: The electromagnetic spectrum.

## Slide 5: The Electromagnetic Spectrum
Frequency and Wavelength: Frequency
  A signal is located on the frequency spectrum according to its frequency and wavelength.
  Frequency is the number of cycles of a repetitive wave that occur in a given period of time.
  A cycle consists of two voltage polarity reversals, current reversals, or electromagnetic field oscillations.
  Frequency is measured in cycles per second (cps).
  The unit of frequency is the hertz (Hz).

## Slide 6: The Electromagnetic Spectrum
Frequency and Wavelength: Wavelength
  Wavelength is the distance occupied by one cycle of a wave and is usually expressed in meters.
  Wavelength is also the distance traveled by an electromagnetic wave during the time of one cycle.
  The wavelength of a signal is represented by the Greek letter lambda (λ).

## Slide 7: The Electromagnetic Spectrum
Frequency and wavelength. (a) One cycle. (b) One wavelength.

## Slide 8: The Electromagnetic Spectrum
  Example:
  What is the wavelength if the frequency is 4MHz?
Frequency and Wavelength: Wavelength
Wavelength (λ) = speed of light ÷ frequency
Speed of light = 3 × 108 meters/second
Therefore:
λ = 3 × 108 / f
λ = 3 × 108 / 4 MHz
= 75 meters (m)

## Slide 9: The Electromagnetic Spectrum
Frequency Ranges from 30 Hz to 300 GHz
  The electromagnetic spectrum is divided into segments:
Extremely Low Frequencies (ELF) | 30–300 Hz.
Voice Frequencies (VF) | 300–3000 Hz.
Very Low Frequencies (VLF) | include the higher end of the human hearing range up to about 20 kHz.
Low Frequencies (LF) | 30–300 kHz.
Medium Frequencies (MF) | 300–3000 kHz AM radio 535–1605 kHz.

## Slide 10: The Electromagnetic Spectrum
Frequency Ranges from 30 Hz to 300 GHz
High Frequencies (HF) (short waves; VOA, BBC broadcasts; government and military two-way communication; amateur radio, CB. | 3–30 MHz
Very High Frequencies (VHF) FM radio broadcasting (88–108 MHz), television channels 2–13. | 30–300 MHz
Ultra High Frequencies (UHF) TV channels 14–67, cellular phones, military communication. | 300–3000 MHz

## Slide 11: The Electromagnetic Spectrum
Frequency Ranges from 30 Hz to 300 GHz
Microwaves and Super High Frequencies (SHF) Satellite communication, radar, wireless LANs, microwave ovens | 1–30 GHz
Extremely High Frequencies (EHF) Satellite communication, computer data, radar | 30–300 GHz

## Slide 12: The Electromagnetic Spectrum
Optical Spectrum
  The optical spectrum exists directly above the millimeter wave region.
  Three types of light waves are:
    Infrared
    Visible spectrum
    Ultraviolet

## Slide 13: The Electromagnetic Spectrum
Optical Spectrum: Infrared
  Infrared radiation is produced by any physical equipment that generates heat, including our bodies.
  Infrared is used:
    In astronomy, to detect stars and other physical bodies in the universe,
    For guidance in weapons systems, where the heat radiated from airplanes or missiles can be detected and used to guide missiles to targets.

## Slide 14: The Electromagnetic Spectrum
    In most new TV remote-control units, where special coded signals are transmitted by an infrared LED to the TV receiver to change channels, set the volume, and perform other functions.
    In some of the newer wireless LANs and all fiber-optic communication.

## Slide 15: The Electromagnetic Spectrum
Optical Spectrum: The Visible Spectrum
  Just above the infrared region is the visible spectrum we refer to as light.
  Red is low-frequency or long-wavelength light
  Violet is high-frequency or short-wavelength light.
  Light waves’ very high frequency enables them to handle a tremendous amount of information (the bandwidth of the baseband signals can be very wide).

## Slide 16: The Electromagnetic Spectrum
Optical Spectrum: Ultraviolet
  Ultraviolet is not used for communication
  Its primary use is medical.

## Slide 17: Bandwidth
Bandwidth (BW) is that portion of the electromagnetic spectrum occupied by a signal.
Channel bandwidth refers to the range of frequencies required to transmit the desired information.

## Slide 18: Bandwidth
More Room at the Top
  Today, virtually the entire frequency spectrum between approximately 30 kHz and 300 MHz has been spoken for.
  There is tremendous competition for these frequencies, between companies, individuals, and government services in individual carriers and between the different nations of the world.
  The electromagnetic spectrum is one of our most precious natural resources.

## Slide 19: Bandwidth
More Room at the Top
  Communication engineering is devoted to making the best use of that finite spectrum.
  Great effort goes into developing communication techniques that minimize the bandwidth required to transmit given information and thus conserve spectrum space.
  This provides more room for additional communication channels and gives other services or users an opportunity to take advantage of it.

## Slide 20: Bandwidth
Spectrum Management and Standards
  Spectrum management is provided by agencies set up by the United States and other countries to control spectrum use.
    The Federal Communications Commission (FCC) and the National Telecommunications and Information Administration (NTIA) are two agencies that deal in spectrum management.
  Standards are specifications and guidelines necessary to ensure compatibility between transmitting and receiving equipment.

## Slide 21: Need for modulation
Practically speaking, modulation is required for;
High range transmission
Quality of transmission
To avoid the overlapping of signals.

## Slide 22: Need for modulation

## Slide 23: Need for modulation

## Slide 24: Need for modulation

## Slide 25: A Survey of Communications Applications
Simplex
  AM and FM broadcasting
  Digital radio
  TV broadcasting
  Digital television (DTV)
  Cable television
  Facsimile
  Wireless remote control
  Paging services
  Navigation and direction-finding services
  Telemetry
  Radio astronomy
  Surveillance
  Music services
  Internet radio and video

## Slide 26: 1-8: Jobs and Careers in the Communication Industry
The electronics industry is roughly divided into four major specializations:
  Communications (largest in terms of people employed and the dollar value of equipment purchased)
  Computers (second largest).
  Industrial controls.
  Instrumentation.

## Slide 27: Careers in the Communication Industry
Types of Jobs
  Engineers design communication equipment and systems.
  Technicians install, troubleshoot, repair, calibrate, and maintain equipment.
  Engineering Technicians assist in equipment design, testing, and assembly.

## Slide 28: A Survey of Communications Applications
Duplex
  Telephones
  Two-way radio
  Radar
  Sonar
  Amateur radio
  Citizens radio
  Family Radio service
  The Internet
  Wide-area networks (WANs)
  Metropolitan-area networks (MANs)
  Local area networks (LANs)

## Slide 29: Careers in the Communication Industry
Types of Jobs
  Technical sales representatives determine customer needs and related specifications, write proposals and sell equipment.
  Technical writers generate technical documentation for equipment and systems.
  Trainers develop programs, generate training and presentation materials, and conduct classroom training.

## Slide 30: Careers in the Communication Industry
Major Employers
  The communication electronics industry is made up of the following segments:
    Manufacturers
    Resellers
    Service Organizations
    End users

## Slide 31: Careers in the Communication Industry
Structure of the communication electronics industry.